## Slide 1
LIMIT-CYCLE BEHAVIOR
in an 8-bit Fixed-Point IIR Filter
COURSE
Digital Signal Processing ECA0905
ASSESSMENT
CO3 – AT3 Error Analysis Task
QUESTION
Question 38 10 Marks
Name: K YOGESWARAN
Register No.: 192412615

## Slide 2
Problem Statement
What is happening in the DSP system?
INPUT
Eventually, x[n] = 0
FILTER
8-bit fixed-point IIR filter
OUTPUT
y[n] = 0.0156 still remains
x[n] = 0 but y[n] = 0.0156
• Determine whether the cause is limit-cycle behavior, overflow, or an implementation error.
• Justify the diagnosis using finite-word-length DSP concepts.

## Slide 3
Error Identification
The strongest diagnosis from the given evidence
MOST LIKELY CAUSE
Zero-input limit-cycle behavior caused by finite-word-length effects.
WHY?
A small non-zero output persists even after the input becomes zero.
Ideal: x[n]=0 → y[n] → 0
Observed: x[n]=0 → y[n]=0.0156
• The persistent low-level output is consistent with finite-precision feedback in an IIR filter.

## Slide 4
Root Cause Analysis
Feedback + finite precision creates the residual
y[n] = Σ bₖx[n−k] − Σ aₖy[n−k]
Zero input
x[n]=0
Feedback
Previous y[n] remains
Quantization
Finite word length
Residual
Small error
Persistence
Residual is fed back
yq[n] = Q{y[n]}
• The quantized residual can be regenerated by the IIR feedback path, producing a persistent non-zero output.

## Slide 5
Why It Is NOT Overflow
The observed value does not indicate range exceeding
|y[n]| = 0.0156
OVERFLOW USUALLY MEANS
Calculated value exceeds the representable numerical range.
POSSIBLE EFFECTS
Wrap-around Sign reversal Saturation Large numerical errors
THIS CASE
0.0156 is a very small value. No range-exceeding behavior is described.
Conclusion: Overflow is unlikely

## Slide 6
Why It Is NOT Primarily an Implementation Error
What would an implementation error look like?
• Incorrect feedback coefficients
• Incorrect sign in the difference equation
• Incorrect scaling
• Incorrect memory/register update
• Incorrect quantization implementation
GIVEN BEHAVIOR
8-bit fixed-point + IIR feedback + zero input + persistent small output
Most justified diagnosis
Finite-word-length limit-cycle behavior

## Slide 7
Correction & Prevention
How to reduce the finite-word-length effect
1 Increase Word Length
Use 16-, 24-, or 32-bit precision.
2 Proper Quantization
Prefer appropriate rounding over simple truncation.
3 Proper Scaling
Scale signals and coefficients to preserve resolution and avoid overflow.
4 Higher Feedback Precision
Keep extra internal precision in the sensitive feedback path.
5 Saturation Arithmetic
Protect against wrap-around when actual overflow occurs.
Higher precision → lower quantization error → fewer limit cycles

## Slide 8
Final Diagnosis & Conclusion
Answer to Question 38
FINAL DIAGNOSIS
Zero-input limit-cycle behavior due to finite-word-length effects in the 8-bit fixed-point IIR filter.
Ideal: x[n]=0 → y[n] → 0
Observed: y[n]=0.0156 persists
• Overflow is unlikely because the observed value is very small and no range-exceeding behavior is indicated.
• No implementation error is indicated by the given information.
• Increasing word length, proper rounding/scaling, and higher feedback precision can reduce the effect.
Therefore: Limit-cycle behavior is the most justified answer.

## Slide 9
THANK YOU
Questions & Discussion
ECA09 • CO3-AT3